## Slide 2: Drone basics
Presentation is done by Dusan Glumac Teodora Zivkovic Nikola Aleksic Matej Milovanovic Nina Pantic Milica Roncevic Andrea Stefanovic
prof Dejan Crnoglavac

## Slide 3: What is drone?
An unmanned aerial vehicle is an aircraft operated by a operator, a person with remote signal transmission from the ground.
The flight of UAVs may be controlled either autonomously by onboard computers or by the remote control from a pilot on the ground or in another vehicle.

## Slide 4: History of drone
The earliest recorded use of an unmanned aerial vehicle for warfighting was occurred in July 1849,serving as a balloon carrier (the precursor to the aircraft carrier) in the first offensive use of air power in naval aviation.
UAV innovations started in the early 1900s, and originally focused on providing practice targets for training military personnel. UAV development continued during World War I, when the Dayton-Wright Airplane Company invented a pilotless aerial torpedo that would explode at a preset time.

## Slide 5: Classification
UAVs typically fall into one of six functional categories: -Combat-providing attack capability for high-risk missions -Reconnaissance – Unmanned reconnaissance aerial vehicle providing battlefield intelligence. -Target and decoy- providing ground and aerial gunnery a target that simulates an enemy aircraft or missile. -Logistics – delivering cargo -Civil and commercial UAVs – agriculture, aerial photography, data collection. -Research and development

## Slide 6: Drone components

## Slide 7: Drone structure
Due to multiple-rotor structure, their anti-torque moments can be canceled out by each other. Thanks to the simple structure, a multicopter is easy to use and features high reliability and low maintenance cost. But, its payload capacity and the time of endurance are both compromised.

## Slide 8: Multicopters
A multicopter, such as a hexacopter, has multiple propellers to generate the thrust, pitching moment, rolling moment, and yawing moment.
On the other hand, a quadcopter only has four propellers to generate the thrust and the three-axis moments.

## Slide 9: Quadcopter control
For simplicity, the introduction to the flight principle of a multicopter is based on a quadcopter, which is propelled by four propellers. A quadcopter can control four motors to change the propeller angular speeds which further change the thrust and moments. According to the classical mechanic theory, a force can be translated on the rigid body and turn into a force and an associated moment, while the moment can be translated directly into the center axis. As a result, the thrust and moments about its center are regulated. With the changed thrust and moments, the altitude and position of a quadcopter are controlled.

## Slide 10: Drone stability control
Taking the propeller as an example, the reaction torque of this propeller can be translated directly into the center axis, while the translation of the thrust generates a pitching and a rolling moment simultaneously. As there are four thrusts to be regulated, the associated moments can be compensated each other. In the case of hovering flight, the sum of the four produced thrusts compensates for the weight of the quadcopter. The thrusts of four propellers are the same and the moments of four propellers sum to zero.

## Slide 11: Command and Control System
Good Command and Control System is key feature of modern drones. It is used to perform drone in the air from the ground.
Command and Control System consists of:
RC transmitter
Receiver
Autopilot

## Slide 12: RC transmitter
An RC transmitter is used to transmit commands from remote pilots to the corresponding receiver. Then, the receiver, passes the commands to the autopilot after decoding them.

## Slide 13: Receiver
The receiver’s main task is to collect commands from RC transmitter, decode them and send them to the autopilot.
The RC transmitter and receiver communicate by radio waves, and the commonly used frequency is 2.4GHz.
Drone receiver

## Slide 14: Autopilot
A multicopter autopilot is a flight control system used to control the attitude, position, and trajectory of a multicopter. It can be semi-automatically (needs commands from remote pilot) or fully automatically.
Autopilots have a control framework which is often based on Proportional-Integral-Derivative (PID) controllers, leaving parameters to be tuned for different multicopters.

## Slide 15: Fuel

## Slide 16: BASIC FUEL PROPERTIES
Each drone requires a specific propulsion system.

## Slide 17: MAIN FEATURES OF THE BATTERY
Voltage - “Li-Po” batteries voltages range from 3.2V to 4.2V
Capacity - Capacity of the batteries varies from the size and weight of the drone they operate
Maximum battery current – depends on discharge current of the battery and time
Energy density - ratio of the maximum energy and mass of the battery substances - expressed in Wh/kg
The allowed discharge value is considered to ensure that the required energy is available. It is calculated with following equation:
CmAh = E_ (h.batt) / (η_DOD ∙ U_nom) ⋅10 ^ 3

## Slide 18: LITHIUM POLYMER BATTERIES
Lithium polymer batteries (“LiPo” batteries) are a type of battery used in many electronic devices.

## Slide 19
Differences between LiPo batteries and nickel-cadmium and nickel-metal hydride batteries
LiPo Batteries:
Less weight and can be made in almost any size or shape
Higher capacity - more power
Higher discharge rates, meaning they pack more punch
Much shorter lifespan
Sensitive chemistry
Need special care

## Slide 20
NiMH Batteries
Longer lifespan than LiPo
Less sensitive
Simpler chargers and usage
Heavier, and limited on size
Lower average capacity
Lower discharge rates

## Slide 21: Lithium-ion batteries
Lithium-ion batteries (“Li-Ion”) – made in early 20th century, popular in the 1990s.
Lithium-ion batteries - similar structure as lithium-polymer
Differences: in the electrolyte and the frame.
Main advantages of Li-Ion batteries: higher energy density, lack of memory effect, cheaper production
Disadvantages: low safety and decreasing battery capacity through “calendar aging”.

## Slide 22: Hydrogen fuel cells
Hydrogen fuel cell converts the chemical energy into electricity.
It’s kept in a container to provide power.
Combined with oxygen gives energy and water
It’s difficult to handle, makes high temperatures
Benefits of hydrogen cells: pure source of energy, most common resource on Earth, higher energy density, quickly replenished with fuel, hydrogen drones operate at low temperatures, ‘BVLOS’ flights are reachable with hydrogen drones.

## Slide 23: Solar energy as a fuel
The development of solar energy technology made photovoltaic (PB) technology - possible alternative for powering UAVs
Lack of space affect design challenge considering increasing the size of the drone.
Another problem are night flights due to lack of light.

## Slide 24: TYPES OF FUEL CELLS AND METHOD OF SELECTION
For now, the following are considered the best types of propellants:
Batteries:
E_batt = ε_S⋅ m_batt ⋅ η_DOD (1)
Hybrid fuel cell system:
βBatt = P_batt / (P_FC + P_batt) (2)
EFCHS = EFC + Eh.batt (3)

## Slide 25
Hydrogen energy
Volume [L] | Cylinder Mass [kg] | H2 mass [g] | Storrage effect [%] | Energy [Wh] | Specific Enegry Wh∙kg−1Wh∙kg−1
2.0 | 1.2 | 41.7 | 3.5 | 700 | 584
3.0 | 1.4 | 62.5 | 4.5 | 1050 | 750
6.0 | 2.5 | 125.0 | 5.0 | 2101 | 840
6.8 | 2.7 | 141.7 | 5.2 | 2381 | 882
7.2 | 2.8 | 150.0 | 5.4 | 2521 | 900
9.0 | 3.8 | 187.6 | 4.9 | 3151 | 829
Hybrid battery
Eh.batt (EFC) = β_batt / (1-β_batt) FCEFC + (temc⋅PFCHS)

## Slide 26
Limitations and shortcomings of modern batteries and propellants
Problem with batteries is temperature
Extreme temperatures supports the formation of lithium dendrites which lead to various problems.
Optimum temperature - from 10 ° C to 30 ° C.
Charging lithium batteries can also be harmfull
Graphene batteries
Graphene - allotropic modification of carbon in the form of a thin plate.
Atoms are arranged in a hexagon shape.
Properties: excellent thermal and electrical conductivity, high strength and flexibility and very low mass.
Key advantages: smaller weight, faster charging, longer service life (Heat is the main culprit for shortening battery life), much higher energy density, greater safety.
Graphene is still a new material.

## Slide 27
THANK YOU FOR YOUR ATTENTION!